Default detector:
- 64x128 detection window
- rgb color space with no gamma correction
- [-1 0 1] gradient filter with no smoothing
- 16x16 pixels per blocks of four 8x8 pixel cells
- block spacing stride of 8 pixels (4 fold coverage of each cell)
- gaussian spatial window with sigma=8 on the block magnitude
- linear gradient voting into 9 orientation bins 0 – 180
- L2-Hys(Lowe-style clipped L2 norm) block normalization on block histograms
- linear svm

Extra steps:

Color space
rgb preferred over grey scale
take each channel independently and calculate gradient in each channel. Take the one with largest norm as the pixel's gradient.
lab gives same result as rgb

lab color space us designed to approximate human vision. Here, lab color space enhancement(right) is shown to given image (left)
square root gamma compression gives low improvement
gamma encodes luminence

Normalization of blocks
-to reduce illumination and foreground-background constrast.
-similar to histogram stretching

a. L2-norm
v = v / sqrt(2-norm of v + epsilon)

b. L2-Hys
clipping maximum value to 0.2 and renormalizing

window size

16 pixels of boundary around the human

SVM

Type: gaussian kernel svm
soft C=0.01
SVMLight package http://svmlight.joachims.org/ - provides implementations in many languages